## Slide 1
1
AQA
    GCSE
      Design and Technology 8552
Sources, origins and properties
Unit 5E
  Textiles

## Slide 2
Objectives
Understand the processes involved in obtaining raw material from animal, chemical and vegetable sources
Be aware of sustainability issues in textile production, in use and end of life

## Slide 3
Starter
Identify and find the link between each of the images below:

## Slide 4
Raw materials for textiles
Raw materials for textiles can be categorised into:
  Animal sources
  Chemical sources and
  Vegetable sources

## Slide 5
Animal fibres and skin (known as hides) can be processed into fabrics
  Fibres (e.g. wool and silk) are spun to create yarn for fabrics
  Hides or skins are treated to produce goods
Animal sources

## Slide 6
Vegetable sources
Plant or vegetable sources (e.g. cotton, jute, hemp and bamboo) are used in the production of many common fabrics
  Other examples include flax which is made into linen and coir which is made from coconut fibres
  Are these renewable?
  Are they sustainable?

## Slide 7
Chemical sources
Crude oil is used to produce chemicals which are processed into fibres to construct fabrics
  Petroleum is commonly used to produce synthetic threads including nylon, polyester and acrylic
  These are often combined with other fabrics to enhance their properties
  How might their properties be enhanced?

## Slide 8
Aramids
Aramid fibres, used in Kevlar® and Nomex®, are used to create some of the strongest, most heat resistant fabrics on the planet
They are used in:
  Fireproof clothing including uniforms
  Spacesuits
  Tyres and work boots
  Cut resistant gloves
  Stab and bullet proof vests

## Slide 9
Raw materials
Complete Worksheet 1 Task 1
  Animal, Chemical or Vegetable?
  Sort the raw material sources into the correct category
  Match the fabric to the raw material

## Slide 10
How are fabrics processed?
There are many different processes for converting raw materials from their sources
  Weaving
  Knitting
  Carding
  Bonding
  Tanning

## Slide 11
Processing yarns
To produce most fabrics, fibres will need to be processed into yarns
  Yarns can then be woven or knitted into fabric
Fibres
Fabric
Yarn
Spinning
Weaving or knitting

## Slide 12
Most natural fibres come in short hairy strands called staple fibres whereas all synthetic fibres are usually long and smooth – these are called filaments
  Why are staple fibres often more absorbent and warmer?
Staple fibres and filaments
Staple fibres
Filaments
Staple fibre yarn
Filament yarn

## Slide 13
Spinning fibres into yarn
Staple fibres and filaments are spun into longer, stronger yarns which can then be woven together to create fabrics

## Slide 14
Weaving and knitting
Both weaving and knitting can be done by hand or by machine

## Slide 15
Warp and weft
Woven fabric is made of interlocking strands of yarn called the warp and the weft
  A common type of weave is called plain weave
  The warp runs the length of the fabric while the weft runs across the width
Selvedge
Warp threads
Weft threads
Bias

## Slide 16
Twill weave
Twill weave uses a different pattern which creates different functional and aesthetic properties
  Can you spot the difference?
Plain weave
Twill weave

## Slide 17
Worksheet experiment
Take a swatch of woven fabric
  Is it plain weave, twill weave or another kind of weave?
  Dissect the swatch into yarn and then into fibres
Use your findings to complete Tasks 2 and 3

## Slide 18
Making felt
Felting is a process where staple fibres are randomly interlocked and compressed to form a matted fabric or 3D product
  Felting can be done by hand or by machine
  What are common uses for felted fabrics?

## Slide 19
Tanning leather
Animal skins or pelts are preserved with a chemical process called tanning
  Raw hides are cleaned, soaked in lime to remove hair and salted to help chemicals penetrate the pelt
  Prepared hides are treated with acid and chromium to produce “wet-blue” leathers
  These are then dried, softened and buffed to a workable finish

## Slide 20
Bonded fabrics
These fabrics are created by fusing fibres together using heat, stitching, adhesives or chemicals
  They are often used in textiles for interfacing and in disposable clothing and cleaning fabrics
  What properties make bonded fibres suitable for cleaning cloths?

## Slide 21
Flame retardants
All fabrics can be treated with flame retardants
  By law (since 1988) certain soft furnishing and upholstered furniture must be treated with flame retardants to reduce the risk of fire or burns
  Examples of use include sofas and curtains

## Slide 22
Environmental factors
What is the true cost of textile production to people and the planet?
  How can the sustainability of textile production be increased?

## Slide 23
Ethical considerations
Land and resources in developing countries are used to create products for western markets
  Would you buy a garment made using child labour?

## Slide 24
Lifecycle analysis
A lifecycle analysis helps you to understand the environmental impact of a product
  Sourcing raw materials
  Manufacture
  Distribution
  Use
  Recovery
Why is Use one of the most environmentally significant phases of a textile product’s life cycle?

## Slide 25
Sustainable or renewable?
What is the difference between sustainability and renewability?
  Is cotton production sustainable, renewable or both?
  Think of one resource that is sustainable but not renewable

## Slide 26
Worksheet 1
Complete Task 4

## Slide 27
There is hope…
Many companies are starting to make changes in their practices
Many consumers are changing their habits as environmentalists work to raise awareness